Five years use of Pulse Doppler RADAR- technology in debris-flows monitoring in comparison with other well established technologies.

Richard Koschuch1, Michael Brauner2, Kaiheng Hu3 and Johannes Hübl4

1 IBTP Koschuch e.U., Langegg 31, 8463,  Leutschach, Austria

2 ÖBB-Infrastruktur AG, Praterstern 3, 1020, Vienna, Austria

3 Institute of Mountain Hazards and Environment, Chinese Academy of  Sciences Chengdu, 610041, China;

4 Institute of Mountain Risk Engineering, Department of Civil Engineering and Natural Hazards, University of Natural Resources and Life Sciences (BOKU), Peter Jordanstraße 82, 1190, Vienna, Austria

Automatic monitoring of alpine mass movement is a major challenge in dealing with natural hazards. The presented research project shows a new approach in alarming technology for debris flow by using a high-frequency Pulse Doppler RADAR. The detection system was implemented on 3 places (2 in Tirol/Austria within the monitoring systems of the IAN/BOKU; 1 in Dongchuan/China within the monitoring systems of the IMHE/Chinese Academy of Science) in order to prove the applicability of the RADAR in monitoring torrential activities (e.g. debris-flows, mudflows, flash floods, etc.). The main objective is to illustrate the principles and the potential of an innovative RADAR system and its versatility as an automatic detection system for fast (> 1 km/h – 300 km/h) alpine mass movements of any kind. The high frequency RADAR device was already successfully tested for snow avalanches in Sedrun/Switzerland (Lussi et al., 2012), in Ischgl/Austria (Kogelnig et al., 2012).

The experience of the five year showed the enormous potential of the presented  RADAR technology in use as an independent warning and monitoring system in the field of natural hazard. We have been able to measure water level changes, surface velocities and several debris flows and can compare this data with the other installed systems.