## Slide 1
8 years experience in avalanche detection
by using a Pulse Doppler Radar
DI Dr. techn. Koschuch Richard
IBTP Koschuch e.U.
Langegg 31
A-8463 Glanz an der Weinstraße
+ 43 / 699 18448542
office@ibtp-koschuch.com
www.ibtp-koschuch.com
www.avalancheradar.com
<Foliennummer>/31

## Slide 2
Principle of the Pulse Radar
The RADAR emits modulated pulses
Notes: Spezialisten aus den Bereichen Radartechnik, Elektronik, Weltraumforschung, Softwareentwicklung und Logistik

## Slide 3
Principle of the Pulse Radar
The RADAR emits modulated pulses
Max. measurement distance R = 5 km
Notes: Spezialisten aus den Bereichen Radartechnik, Elektronik, Weltraumforschung, Softwareentwicklung und Logistik

## Slide 4
Principle of the Pulse Radar
The RADAR emits modulated pulses
Max. measurement distance R = 5 km
RG-length rRG=15-250 m
Notes: Spezialisten aus den Bereichen Radartechnik, Elektronik, Weltraumforschung, Softwareentwicklung und Logistik

## Slide 5
Principle of the Pulse Radar
The RADAR emits modulated pulses
Max. measurement distance R = 5 km
RG-length rRG=15-250 m
Velocities up to 300 km/h are detected simultaneously in each RG
v1
v2
v3
Notes: Spezialisten aus den Bereichen Radartechnik, Elektronik, Weltraumforschung, Softwareentwicklung und Logistik

## Slide 6
Principle of the Radar
The RADAR emits modulated pulses
Max. measurement distance R = 5 km
RG-length rRG=15-250 m
Velocities up to 300 km/h are detected simultaneously in each RG
If there is a hazardous event (fast moving objects), data run trough an algorithm and in case an alarming trigger is activated.
Notes: Spezialisten aus den Bereichen Radartechnik, Elektronik, Weltraumforschung, Softwareentwicklung und Logistik

## Slide 7
Principle of the Pulse Radar
Snow Avalanches
Debris Flow
Water Level Detection
Rockfall
Man Detection
Rain Detection
Notes: Spezialisten aus den Bereichen Radartechnik, Elektronik, Weltraumforschung, Softwareentwicklung und Logistik

## Slide 8
Specification
Parameter | Quantity | Tolerance | Unit
Mode | Pulse/PCM |  | 
Frequency | 10.0-10.5 |  | GHz
Power C. | 40 | < | W
Range | 30-5000 |  | m
Targetsize | 1 | min > at 2km | m²
 | 0,25 | min > at 1km | m²
Velocity | 0,2-100 | min/max | m/s
RG | 128 | max | 
RG-length | 15-250 | min/max | m
Notes: Spezialisten aus den Bereichen Radartechnik, Elektronik, Weltraumforschung, Softwareentwicklung und Logistik

## Slide 9
Function I: Mobile RADAR
Mobile Radar in Action; Fotos Daniel Lussi, SLF

## Slide 10
Function I: Mobile RADAR
Mobile Radar in Action; Fotos Daniel Lussi, SLF

## Slide 11
Function I: Mobile RADAR
Mobile Radar in Action; Fotos Daniel Lussi, SLF

## Slide 12
Function II: Fix Installation Ischgl

## Slide 13
Function II: Fix Installation Ischgl

## Slide 14
Function II: Fix Installation Ischgl

## Slide 15
Function II: Fix Installation Ischgl

## Slide 16
Function II: Fix Installation Ischgl

## Slide 17
Function II: Fix Installation Ischgl

## Slide 18
Function II: Fix Installation Ischgl

## Slide 19
Function II: Fix Installation Ischgl

## Slide 20
Function II: Fix Installation Ischgl

## Slide 21
Function II: Avalanche during heavy Rainfall
Velocity Spectrum
Avalanche RG14

## Slide 22
Function II: Avalanche during heavy Rainfall
Velocity Spectrum
Rain RG1

## Slide 23
Function II: Installation Pitztal

## Slide 24
Function II: Installation Pitztal

## Slide 25
Project Avalanche Detection Systems SLF
Summery Comparison Tests SLF:

## Slide 26
Master Thesis Boku Vienna
Summery Thesis Christian Kienberger 2013:
„Evaluation of Avalanche Detection Systems and Development of a Plan for a Simple Detection System“
Avalancheradar

## Slide 27
Avalanche Detection Radar
Place of Radar | Years of operation | Alarm and Avalanche | False Alarm | No Alarm but Avalanche
Sedrun | 2010-2012 | 12 | 7* | 0
Ischgl | 2011- | 102 | 3** | 0
Kaunertal | 2012- | 8 | 1*** | 0
Kappl | 2012- | 287 | 7** | 2****
Avalanche Detection Rate for installed Radar Systems:
* all alarms within one hour caused by a truck covering time by time the detection- cone
** all alarms on one evening within 2 hours caused by a heavy rain shower in January; new algorithm can handle this.
*** Module defect
**** Radar detected the avalanche, but the phone connection was broken

## Slide 28
Reliable recognition of avalanches, mudslides, debris flow and water level changes
  Minimization of false alerts
Low transmitted power
  Energy and environment friendly
Possibility of mobile operations
Low installation requirements
  Only a mast and a power supply of 40 W
Technology and Benefits of the System I
Notes: Geringe Sendeleistung: 100mW

## Slide 29
Recognition of risk in real time (within a second)
  maximum warning
Multifunctional alert system
  trigger to local signal systems
  real time information to central warning institutions via SMS, Email, LiveViewer…
  fast, save and regardless from weather conditions
Technology and Benefits of the System II
Notes: Erkennungszeitraum: 1 – 2 Sekunden
Multifunktionales Warnsystem
  Lokale Signaleinrichtungen (z. B. Ampelanlagen zum Sperren einer Straße, Signalhörner)
  Relaisausgänge
  Mobilfunktechnik (SMS, Email)
  Landeswarnzentrale, Straßendienst, Bergrettung, etc.
Bilderfassungseinheit (Ermittlung des Verursachers, Detektion von Verschütteten, etc.)

## Slide 30
Conclusion
We are able to detect reliable even smallest avalanches in any weather conditions
The Radar-availability is very high and is continuously checked online
The falsalarm quote is extremely low
We can provide an optimal setup for each location
Notes: Spezialisten aus den Bereichen Radartechnik, Elektronik, Weltraumforschung, Softwareentwicklung und Logistik

## Slide 31
Thank You
Thank You
Notes: Spezialisten aus den Bereichen Radartechnik, Elektronik, Weltraumforschung, Softwareentwicklung und Logistik